## Slide 1
10.8.21 TFF trial : reg plasmids: hTERT-CMV, fibracel , 2.3x108 cells, 2.5mg DNA, PEI;DNA ratio- 1;1
Clarification: Watersep 0.45uc 320.6 cm^2
Concentration and Diafiltration: TangenX cassettes, 100um, pes, 0. 1m^2
10.8.21 Purification steps (Q-XL)
1st Run
Conductivity 7 mS/cm
Conductivity 5.6 mS/cm
Flow-Through
Wash
Analysis:
qPCR
2D ddPCR
Western
Ruby

## Slide 2
qPCR
2D ddPCR
Full capsids
Conclusions:
TangenX cassette was hacked – probably due to long CIP
0.45um pore size is suitable for initial clarification
Sample that was diafiltrated w/o initial concentration kept the capsids intact – might need to consider lowering flow-rate for optimization
In purification step: decreased conductivity and prolonged wash step may improve recovery acc. To ddPCR results
Western blot
FPLC-1
FPLC-2
FPLC-3
FPLC-4

## Slide 3
17.8.21 Purification steps (Q-XL)
17.8.21 TFF trial : reg plasmids: hTERT-CMV, BioNoc , 3.2x108 cells, 2.5mg DNA, PEI;DNA ratio- 1;1
Clarification: Watersep 0.45uc 320.6 cm^2
Diafiltration: TangenX cassettes, 100um, pes, 0. 1m^2
Analysis:
qPCR
2D ddPCR

## Slide 4
17.8.21 TFF trial : reg plasmids: hTERT-CMV, BioNoc , 3.2x108 cells, 2.5mg DNA, PEI;DNA ratio- 1;1
qPCR
2D ddPCR
Full capsids
Conclusions:
0.05um pore size is TOO small for initial clarification
Sample that was diafiltrated w/o initial concentration kept the capsids intact
Flow-rates through TangenX cassette were decreased and that lowered the efficiency of the diafiltration.
In purification step: 6.75mS/cm conductivity and prolonged wash did improve amplitude and recovery (qPCR)
ddPCR results needs to be repeated (needed further dilutions for accuracy)
The quantification is not precise due to lack of sufficient dilutions.
Repeat was failed due to technical issues